## Slide 1: Gator Training
Department of Environmental Health and Safety
(412) 624-9505
www.ehs.pitt.edu

## Slide 2: Introduction It is the responsibility of the Department to ensure training is implemented to all employees/department affiliates that are operating a utility vehicle. This document provides basic guidelines and safe operating practices for Utility vehicles owned and operated by the University of Pittsburgh. These guidelines are examples of some of the requirements and are not all inclusive.
This training establishes proper safety procedures and practices when utilizing Gators, Golf Carts, or Mini Trucks on campus.
All utility vehicles must have a strobe light placed on the utility vehicle as applicable.
All plated utility vehicles must be registered with the Office of Fleet Services.

## Slide 3: Gators, Golf Carts, or Mini Truck Types
PICTURED: GEM Low Speed Vehicle

## Slide 4: Gators, Golf Carts, or Mini Truck Types Characteristics
  Compact, powerful, and versatile machines
  Commonly gasoline, diesel, or electric powered
  Could be 2-wheel, 4-wheel, all-wheel drive, or tracked
  Operates like a car/truck with a steering wheel, accelerator foot pedal, and a break foot pedal
  High/low range & reverse transmission
  Side by side or bench seating with seat belts
  All-terrain tires with 20 PSI or less tire pressure
  Hauling capability with cargo box
  Towing capability with hitch
  Easy to operate with training

## Slide 5: Permissible Use of UTV
Utility Type Vehicles may be operated as follows:
    To transport people, equipment, or supplies
    When operated by an eligible UTV operator
    When UTV is properly serviced and equipped with all necessary equipment
    On walkways or side walks in such a manner that they do not impede or interfere with normal pedestrian traffic, to a maximum speed of 5 mph
    With the utmost courtesy, care, and consideration for the safety of pedestrians who will be always given the right of way

## Slide 6: Permissible Use of UTV
Restrictions while operating UTV
    Equipment should not be modified in any way that will affect the recommended mode of operation, speed, and/or safety
    Never wear headphones, use cell phones, or any other device that may restrict hearing or control while operating.
    Don’t talk/text and drive! Even if the call concerns important work-related business – pull over first!
    Never operate any equipment under the influence of drugs or alcohol. This can include any prescription medication that makes you drowsy, dizzy, or impaired.
    Smoking is prohibited inside UTVs.
    Talk to your supervisor if you don’t feel you can operate an UTV.

## Slide 7: Permissible Use of UTV
Eligibility to Operate
    University employees and approved affiliates are the only permitted drivers.
    Employee must have a valid driver’s license. Driver’s license must be processed through the Office of Fleet Services. For more information, Department designee should email fleetservices@bas.pitt.edu
    Obey all traffic regulations
    Complete training annually
    Ability to operate vehicles in a safe and responsible manner.

## Slide 8: Potential Hazards
  Rolling over on steep slopes, dangerous terrain, or fast turns
  Collision with another vehicle or object
  Pinch points, cut points, wrap points, and burns while working with the UTV
  Fluids under high pressure or other stored energy
  Injury to driver and passengers from shifting loads in cargo area
  Injury from falling from the UTV when mounting and dismounting
  Injury to the eyes from dust and insects while UTV is in motion
  Injury to pedestrians from being struck by the UTV or from loads falling off UTV

## Slide 9: Prior to Use
  Understand differences between UTV and a highway vehicle
    UTV has:
      Smaller wheelbase
      Higher center of gravity
      Center of gravity is always shifting during operation
      Low pressure, off highway tires
  Load Capacity
    Know the manufacturer’s load weight limit and do not exceed
      Overloading decreases your ability to maneuver and operate safely
    When hauling cargo, the center of gravity is raised and moves towards the rear axle, increasing the risk of tip-over in any direction
    Secure all equipment and supplies to prevent objects from falling out or striking people
    Only one passenger per seat
    No riding on back, front, or sides
    Loads are only to be loaded, repositioned, or unloaded when the UTV is in park or neutral

## Slide 10: Prior to Use
  Check for proper operation of critical equipment
    Lighting
      Head lights
      Taillights
      Brake lights
      Turn signals
    Brakes/Parking Brake
      Work smoothly without noise or pulling
    Reflector & Sign
    Steering
    Horn Tire Inflation and condition
    Fuel level or Battery power
      Batteries
        Never use batteries to power other devices
        Never use extension cords
        Never attempt to check or add fluid to the battery
        Chargers should be plugged directly into a ground fault circuit interrupter receptacle
        Recharging outlets must be designed to be locked when not in use
    Check for puddles, leaks, odors, strange sounds, or behavior that can indicate a large mechanical problem

## Slide 11: Prior to Use
  Towing capacity
    Do not tow a load that exceeds the maximum towing load as specified by owner’s manual
    Weight of towed load (trailer + cargo) must never exceed the vehicle payload
    Travel at a speed low enough to maintain control
    Stopping distance increases with speed and weight of towed load
      Allow extra time and distance to stop
    Excessive towed load can cause loss of traction and loss of control on slopes
    Tow only with an approved hitched designed for towing
  Attachment use
    Read attachment manual and follow instructions and warnings
    Can include snowplows, sprayer units, dry material spreaders, winches and roof racks
    Must be compatible with UTV
    Verify that all connections are secure, and attachment responds properly to controls
    Attached changes can affect:
      Intended use of UTV
      Weigh or balance of machine
      Can alter machine controls, performance, and reliability

## Slide 12: Safe Driving
  Importance of safe driving
    Being focused and giving your full attention to driving
    No texting or talking on your cell phone while behind the wheel. If you are involved in an accident while operating a vehicle on University business and you are conducting a call, texting, or accessing and using internet transmissions, you will be subject to corrective actions up to and including termination. https://www.pts.pitt.edu/mobility/fleet-services/mobile-device-guidelines
    Make the safety of yourself and others your top priority.
  Driving Safely on Public Roads – OAKLAND CAMPUS
    UTVs must be driving at a safe speed given the operating conditions
      Excessive speed requires a greater stopping distance and increases risk of tip over on corners
    Maintain a safe distance behind other vehicles
    Refrain from traveling via roadways at peak traffic hours if possible
    Stay alert for traffic and roadside obstacles

## Slide 13: Safe Driving
  Driving Safely on University Property
    When driving on travel path or sidewalk, do not exceed the speed of bicyclists or pedestrians
    Do not block sidewalks or travel paths
    Use extreme caution when approaching pedestrians and always give them right of way
    Utilize curb cuts when navigating from roadways to sidewalks. Jumping curbs can cause damage and compromise vehicle control.
    When leaving UTV, the vehicle must be taken out of gear, ignition must be turned off, and parking brake applied. Remove and secure ignition key from unauthorized use.
    Avoid areas that are highly congested with pedestrians
    If driving in a congested area, use a spotter to assist with crowd control
  Driving Safely Off Road
    Be alert to ground hazards, look ahead at the terrain
    Watch for holes, ruts, and other obstacles
    Watch for uneven surfaces, drop offs, and overhead clearance obstructions
    Reduce speed according to the terrain and visibility conditions
    Avoid slopes if possible. Travel up and down on slopes, not sideways.
    Never cross a body of water where the depth is unknown

## Slide 14: Safe Driving
  Defensive Driving
    Stop at all blind intersections and then proceed with caution
    Yield to pedestrians
    When approaching individuals from behind, sound the horn and do not proceed until eye contact has been made
    Never drive toward an individual standing in front of a fixed object
    Ensure other drivers have seen the UTV prior to progressing
    Verify safety prior to all turns. Look over shoulder in direction of travel prior to turn to check for motor vehicles, pedestrians, and bicyclists.
    Ensure use of seat belts if equipped.
  Passenger Safety
    Keep head, legs, and arms within cab
    Remain in seats
    Do not exceed manufacturer’s load limits (Number of passengers or weight)
    Use seat belts if provided
    Warn passengers of rough terrain that way cause you to bounce or swerve
  Parking
    When mounting or dismounting vehicle, it must be placed in the neutral or park position and shut off
    Never park within 20 feet of entrances/exits of buildings (except at loading docks or approved parking spots)
    Do not block entrances, stairways, fire exits, fire hydrants, disability ramps or main thoroughfares

## Slide 15: Maintenance
  Follow owner’s manual for maintenance schedule
  Records of all recommended maintenance and repair should be kept by the department

## Slide 16: Accidents
  Report any accident immediately to:
    Your supervisor
    Environmental Health & Safety
    Complete a Vehicle Accident Report Form (VARF) by following the guidelines https://www.pts.pitt.edu/mobility/fleet-services/reporting-vehicle-accidents
    PLEASE WRITE UTILITY VEHICLE ACCIDENT ON TOP OF VARF
  Any accident involving a pedestrian or car must be reported to Pitt Police

## Slide 17: Questions
Please direct any questions to your supervisor or the Department of Environmental Health & Safety
safety@pitt.edu
412-624-9505